## Slide 1: intel’s makers community board design with eagle
Gil Tal.
Sep 2022

## Slide 3: Course agenda:
Basics (very basics) electronics
What is a PCB?
Board producing process
Schematic
Design rules
The Physical Board
Placement
Routing
Production
Board power on and debug

## Slide 4: OHM law
V = R*I (URI)

## Slide 5: Basic components
A resistor is a passive two-terminal electrical component that implements electrical resistance as a circuit element.
Basically, turns electrical energy into heat.
Measure unit: ohm
Usages: Limit current, drop voltage level, Pull up/down floating signals
A capacitor is a device that stores electrical energy in an electric field. It is a passive electronic component with two terminals.
Measure unit: Farad
Usages: Handle power supply surge, very fast absorption of electrical energy (also fast discharge), along with a resistor a simple reset at power on

## Slide 6
A diode is a two-terminal electronic component that conducts current primarily in one direction (asymmetric conductance); it has low (ideally zero) resistance in one direction, and high (ideally infinite) resistance in the other.
A transistor is a semiconductor device used to amplify or switch electronic signals and electrical power

## Slide 7
Open drain buffer: Either short to ground or float the output
A pull up resistor is needed to drive logic 1
Bi-Directional I/O
Tri state buffer:

## Slide 8: PCB
Printed circuit board
Mechanically supports and electrically connects electrical or electronic components
Using conductive tracks, pads and vias
May be composed from few layers of copper laminated onto and/or between layers of a non-conductive substrate

## Slide 9: PCB - Structure
Standard thickness 1.6mm
Suggested trace width for cheap PCBs 5-6 mil (check with manufacturer)
Via connects traces between different layers
Pads are used for soldering devices
Via
Via
Via
Trace
Pads

## Slide 10: Board producing process
Block diagram
Components
Pick up
Schematic
ERC +
Netlist
Board
creation
Placement
Routing
DRC
Generate
Production
Files
Send board
To production
Purchase
components
Assembly
Power On

Set rules
For routing

## Slide 11: Schematic – Step 1
Draw a block diagram (ESPboy)

## Slide 12: ESPboy

## Slide 14: Components pickup:
I/O Voltage
What types of I/Os does it have
Power supply voltage
Type of packages (Next slide)
Type of I/Os (especially open drain needs attention)
Does it use an output enable? If yes check polarity
Does it need reset? If yes check polarity
Does it need a pull up\dows for some of its signals? (interrupts for example)
Does it have a sample at reset pins?
Check if it has I/Os that functions differently under reset?
For I2C devices check their address

## Slide 15: Different types of packages
Through hole (TH)
SMT (Surface Mount)
BGA (Ball Grid Array)

## Slide 16: What we need for the ESPboy?
ESP8266 module
LCD screen: 1.44” 64K colors, SPI interface
I/O expander, I2C interface, PCF8574
Tactile joystick
2 low profile cherry-MX buttons
2 SMT switches
Buzzer

## Slide 17: Schematic – Rules and caveats
Two outputs cannot be connected to each other
  It can happen without paying attention
Do not leave a floating input signals
I/Os voltage level must be suitable
  Some devices has I/Os that can tolerate high voltage
Special I/Os needs special attention:
  Open drain must have pull ups (interrupts)
  I/Os which have output enable must have a pull up/down
  Sample at reset I/Os
Most component need a capacitor\s placed near the power supply
I2C devices addresses needs coordination

## Slide 18: Schematic – Step 3
Create a new project in Eagle
  Draw your schematic
  Components needed must be in the library

## Slide 19: Board – Step 1
In Eagle generate the board

## Slide 20: Board – Step 2
Set
the physical size of the board
Set
the number of layers (default is 2, we will not use more than 2)
Set
the net classes: (Edit->Net classes)
Power
Regular signals (default)
Custom if needed
Set
the project’s general settings:
Edit->Design Rules

## Slide 21: Board – Step 3 (Placement)
Locate your components on the physical board
Try to keep them all on the components side (upper layer)
Set drills for mounting
Do a placement physical check
  Print the board in 1:1 ratio (Also use the manufacturing view)
Create planes if needed

## Slide 22: Board – Step 4
Routing:
Net List check (if not done yet)
Route (use the auto router)
Complete un routed signals
Fix whatever needed
Run an ERC/DRC check
Add text (tPlace \ bPlace only!)
Generate the production file
Send to production and prayer 